CURLING PHYSICS

FORWARD VELOCITY OF A SINGLE STONE
- Coefficient of friction:
  - 0.0168 (http://hypertextbook.com/facts/2004/GennaAbleman.shtml)
  - 0.00200 (http://www.physicsforums.com/showthread.php?t=544331)
- Mass of a curling stone 19 kg (ish)
- Normal force (Fn)
  F = ma = (19 kg) (- 9.8 m/s) = -186.2 N
- Force of friction
  F_f = %mu F_n = (0.0168) (-186.2 N) = - 3.13 N
- Initial velocity (from the internet):
  - 2.5 m/s
  - 3.0 m/s
  - 2.46 m/s
- Initial velocity for a T-weight throw (by physics and above values)
  d = 130 ft = 39.6 m " (From hack to t-line)"
  m = 19 kg
  F_f = -3.13 N
  v_f = 0 m/s
  v_i = ?
  d = {v_f ^2 - v_i^2} over {2 a}
  v_i = sqrt{v_f^2 - 2 a d}
  v_i = sqrt{- 2 a d}
  F = m a
  a = F over m
  v_i = sqrt{- 2 {F d} over m} = sqrt{- 2 {(-3.13 N) (39.6 m)} over (19 kg)} = 3.6 m/s

CURL OF A SINGLE STONE
Higher velocity = less curl

COLLISION OF TWO STONES: TRANSFER OF LINEAR MOMENTUM
- The following calculations are for an elastic collision (coefficient of restitution = 1)
- Energy is conserved; the vector momentum is conserved (i.e., the sum with the resulting velocity vectors should be the same as with the initial)
- Find unit tangent and normal vector
  - Find normal vector (difference between middles)

COLLISION OF TWO STONES: TRANSFER OF ANGULAR MOMENTUM